## Slide 1: Intelligent Flower Pot
Group 11
Fu Xiao Han
Wong Hi HONG

## Slide 2: Background
Help people take care of their plants
  Lacking attention to their plants in modern world
  Many inexperienced and busy owner of plants

## Slide 3: 4 Major function
Show the parameter of the plants
Monitor the plants by camera
Automatically water plants
Communicate with phone through a web page

## Slide 4: Sensors (DHT11)
Serial connect to STM32
  GPIO (PE.6)
Digital output
detect air temperature and humidity

## Slide 5: Sensors (BH1750)
Serial communication standard (I2C Bus)
  PB.6 —>SCL
  PB.7 —>SDA
Detect luminance

## Slide 6: Soil Moisture Sensor
Analog-to-Digital Conversion (ADC)
  PC.0
Get the converted digital data and reform it to percentage
Detect the soil moisture

## Slide 7: Camera (OV7725)
Connect to camera ports on stm32
Two mode
  color and b/w mode
Can store photo on SD card

## Slide 8: Water pump
5V DC to activate
GPIO connect to 5v electric relay to control the pump
  PA.12 as the control signal for relay

## Slide 9: WiFi module
Connect to the Internet through ESP8266 Module
Communicate with remote server through TCP
Build a webpage
  Real time update sensors’ data
  Support remote observation and water controlling

## Slide 10: Design Diagram
Internet

## Slide 11: Demonstration
Procedure
  1: Choose the type of plants
  2: Enter the monitor mode
  3: Show the parameter of plants
  4.Photograph the plant and store in SD card
  5.Water the plant by button and phone
  6. Automatically water plant
Color mode
B/W mode
Temperature
Humidity
Soil moisture
Luminance

## Slide 12: Difficulties
Wifi module
  Camera occupy many pins in the stm32 (conflict with internal ESP8266)
  Limited performance restrict the I/O amount
Water pump
  Need digital output to control
  Use electronic relay
  Mystery effect on Wifi Module when drived

## Slide 13: Future improvement
Implant more plants information
Add soil fertility parameter (soil conductivity) and PH value